## Slide 1
1 Data Acquisition
Wildfire points 2000–2024 (CWFIS) · Climate (TerraClimate,
ERA5-Land) · Topography (SRTM) · NDVI (Landsat-8)
Land use / land cover (ESRI)
2 Data Preparation
All layers resampled to 1.5 km · raster → point (ArcGIS Pro)
1,992 wildfire and 1,992 non-wildfire points
3 Preprocessing and Feature Engineering
Impute, scale and one-hot encode on training data only
RF-RFE feature selection; the same feature list is applied
to every split to prevent leakage
4 Dataset Split
Training 70% / Testing 30%
10-fold spatial cross-validation (~50 km blocks)
5 Deep-Learning Models
LSTM · Bidirectional LSTM (BiLSTM)
Hyper-parameter optimization by PSO
Model performance acceptable?
6 Validation and Explanation
Accuracy, sensitivity, specificity, precision, F1, ROC-AUC
BiLSTM-PSO test AUC = 0.92
Post-hoc SHAP explanation of influential predictors
7 Susceptibility and Exposure Outputs
Five-class susceptibility maps · district exposure of households,
roads and vegetation · cross-border consistency check
Yes
No
Spatiotemporal
Patterns and Trends
Annual, monthly and
seasonal fire-density
maps (2000–2024)
Theil–Sen slopes with
95% confidence intervals
and Mann–Kendall τ
District-wise and
climatic-variability
analysis